NOTES TO COVER VEHICLE RECOGNITION POWER POINT PRESENTATION

Challenger 2

The superb Challenger 2 (CR2) is the British Army's Main Battle Tank. CR2 is based on the Challenger 1 that served with distinction on operations in the Gulf War and the Balkans.

Only 5 per cent of Challenger 2 components are interchangeable with its predecessor; over 150 major modifications include a completely new turret, L30 CHARM 120mm gun and second generation Chobham armour.

Challenger 2's Thermal Observation and Gunnery (TOGS) displays a magnified image for the commander and gunner. The commander has a gyro-stabilised fully panoramic sight with laser range finder and thermal imager. The gunner is equipped with a gyro-stabilised primary sight with a laser range finder and coaxially mounted auxiliary sight. The driver's position has an image-intensifying day and night periscope, and the loader has a day sight.

| Crew | 4 |
| --- | --- |
| Length | 11.55 m (gun forward) |
| Width | 3.5 m |
| Height to turret roof | 2.49 m |
| Combat weight | 62,500 kg |
| Main armament | 120 mm L30 CHARM (CHallenger main ARMament) Gun |
| Ammunition | 50 rounds - APFSDS, HESH, Soke (Typical) |
| Secondary armament | C-axial 7.62 mm chain gun, 7.62 mm GPMG (turret mounted) |
| Ammunition | 4,000 rounds 7.62 mm |
| Engine | 1,200 bhp Perkins-Condor CV12 |
| Maximum speed | 59 kph |

Scimitar

The vehicle's exceptionally low ground pressure and small size make it useful where the terrain is hostile and movement difficult. Scimitar carries a 30mm Rarden cannon for self-defence. It is used by reconnaissance regiments of the Royal Armoured Corps and 'recce' elements of the armoured infantry.

| Crew | 3 |
| --- | --- |
| Dimensions | 4.9 m (L) x 2.1 m (H) x 2.24 m (W) |
| Ground clearance | 0.35m |
| Combat weight | 8,070 kg |
| Main armament | 1 x 30 mm L21 Rarden cannon |
| Secondary Armament | Co-axial 7.62 mm GPMG, smoke grenades |
| Ammunition carried | 160 rounds of 30 mm, 3,000 rounds of 7.62 mm |
| Engine | Cummins BTA 5.9, 190 hp diesel engine |
| Maximum speed | 80 kph |

Warrior

The Warrior Infantry Fighting Vehicle has the speed and performance to keep up with Challenger 2 Main Battle Tanks over the most difficult terrain, and the firepower and armour to support infantry in the assault.

The Warrior (WR) family of 7 variants of armoured vehicles entered service in 1988 and have proved a resounding success for Armoured Infantry (AI) battlegroups (BG) in the Gulf War, Bosnia and Kosovo and Iraq. They provide excellent mobility, lethality and survivability for the Infantry and have enabled key elements from the Royal Artillery (RA) and Royal Electrical and Mechanical Engineers (REME) to operate effectively within the Battlegroup. A highly successful armoured fighting vehicle, Warrior can be fitted with Enhanced Armour and is continuously being updated; for example, the Battle-group Thermal Imager (BTI) is being fitted to increase its night-fighting capability and is second to none.

Warrior infantry command and section vehicles carry a turret mounted 30 mm Rarden cannon that will defeat light armoured vehicles out to 1,500 m. An 8x magnification image-intensifying night sight is fitted, and eight 94 mm Light Anti-Armour Weapon (LAW) HEAT rockets can be stowed in the vehicle.

Warrior variants include artillery observation post vehicle (OPV) and command post vehicle (CPV), and a REME recovery and repair vehicle. All variants are equipped with a 7.62 mm chain gun. Both chain gun and Rarden cannon have an anti-helicopter capability.

Jackal

Jackal 2 is a high mobility weapons platform, with a unique air-bag suspension system allowing rapid movement across varying terrain.

It is designed to protect personnel against roadside explosions and mine attacks (the chassis of Jackal 2 is heavier than its predecessor to give additional protection).

Used for reconnaissance, rapid assault, fire support and convoy protection Jackal 2 has the capacity to support itself and its crew of three over 800km.

It has a maximum speed of 80mph (129km/h) on roads or 55mph (89km/h) over rough terrain, and weighs seven tonnes.

Jackal 2 is armed with a General Purpose Machine Gun (GPMG) as crew protection and can carry either Heavy Machine Gun (HMG) or Grenade Machine Gun (GMG) as the main weapon system in the fire support role.

The gun ring on Jackal 2 has been moved forward to give a 360º sweep of fire, as opposed to the previous rear-fire only position on the original Jackal.

Jackal 2 is closely related to the new Coyote tactical support vehicle, which is a six-wheel Jackal-based armoured vehicle.

Mastiff

Mastiff is a heavily armoured, 6 x six-wheel-drive patrol vehicle which carries eight people, plus two crew. It is currently on its third incarnation.

It is suitable for road patrols and convoys and is the newest in a range of protected patrol vehicles being used for operations.

With a maximum speed of 90 kph Mastiff is armed with the latest weapon systems, including a 7.62 mm general purpose machine gun, 12.7 mm heavy machine gun or 40 mm automatic grenade launcher.

These wheeled patrol vehicles have a less intimidating profile than tracked vehicles and give commanders on the ground in Afghanistan more options to deal with the threats they are facing.

They have Bowman radios and electronic countermeasures and are fitted with additional armour beyond the standard level to ensure they have the best possible protection.

Mastiff  is just one of a whole range of protected vehicles being used on operations, including Coyote, Husky, Jackal, Panther, Warthog, Wolfhound and Viking.

Improvements on the Mastiff  include:

- Bigger axles

- Up-rated suspension

- Increased electrical power from the alternator 400A vs 200A

- Increased crew capacity 2 + 8 as opposed to 2 + 6 (plus an occasional 7th)

- Increased CES/stowage locations

- Blast attenuating seats

- Fold up seats allowing easier stowage if the vehicle is not full of crew

- New Situational Awareness system incorporating a Thermal Imager for the driver

- Redesigned gunners step

- Electronic Turret Traverse Mechanism

- Engine and fuel tank fire suppression systems.

The vehicles are based on the US Cougar made by Force Protection with the UK integration work carried out by NP Aerospace, based in Coventry.

AS90 Self Propelled Gun

AS90 is a 155mm self-propelled gun that equips six Field Regiments of the Royal Horse Artillery and Royal Artillery.

Fitted with a standard barrel, AS90 can fire the NATO L15 unassisted 155mm projectile (96lbs) 24.7 km. With a long (52 Calibre) barrel the gun can reach out to 30 km using standard ammunition, and 60-80 km with Extended Range (ERA). AS90 is equipped with an autonomous Navigation and Gun Laying system (AGLS) based on the vehicles inertial navigation system, the Dynamic Reference Unit (DRU). All main turret functions are controlled by the Turret Control Computer (TCC).

| Crew | 5 |
| --- | --- |
| Length | 9.07 m |
| Height to turret roof | 2.49 m |
| Width | 3.5 m |
| Ground clearance | 0.41 m |
| Main armament | 1 x L31 39-calibre ordnance |
| Ammunition carried | 48 x 155 mm rounds |
| Secondary armament | 1 x 7.62 GPMG on turret for air defence |
| Engine | Cummins VTA903T turbocharged V8 660 bhp diesel |

Warrior OPV

Variant of the Warrior Infantry Fighting Vehicle

Stormer

The tracked Stormer vehicle provides a mobile platform for the Starstreak High Velocity Missile (HVM) system giving the detachment protection and excellent mobility with eight ready to fire missiles and a further nine stowed inside.

The HVM system is a low level Close Air Defence (CAD) system with a rapid engagement capacity developed and optimised to counter the Attack Helicopter threat. This highly flexible system is also capable of being fired using the Lightweight Multiple Launcher or from the shoulder. The missile employs a system of three dart type projectiles which can make multiple hits on the target. Each of these darts has an explosive warhead.

The system is fitted with a roof-mounted Air Defence Alerting Device, providing target detection and prioritisation. A panoramic weapon sight is located at the front right of the vehicle.

During mid 2009 Stormer will gradually be decomissioned.

| Weight | 13.5 tonnes |
| --- | --- |
| Dimensions | 5.6 m (L) x 3.4 m (H) x 2.8 m (W) |
| Range | 600 km |
| Maximum speed | 80 kph |
| Trench crossing | 2 m |

Titan

Titan is a new armoured engineer vehicle designed to enable troops and vehicles to cross gaps of up to 60 metres by laying a selection of close support bridges. Along with Trojan it gives a common heavy armour fleet based on the Challenger 2 Main Battle Tank chassis.

Titan can carry and lay the current range of in-service close support bridges, providing ground manoeuvre formations with improved capability, giving them greater flexibility.

Improved visibility is achieved by incorporating direct and indirect vision systems including low light, image intensifying and thermal imaging capabilities. The interior, and to some extent the exterior, of the vehicles
have been designed around the crew station positions.

Titan has the flexibility to support a wide range of operations, including humanitarian missions.

| Weight | 62,500 kg |
| --- | --- |
| Carries | BR-90 Close Support Bridges: No. 10 (Length 26 m, span 21-24.5 m); No. 11 (length 16m, span 14.5 m); and No. 12 (length 13.5 m, span 12 m) |
| Road speed | 59 kph |
| Road range | 450 km |
| Engine | Perkins CV12 diesel engine, David Brown TN54 enhanced low-loss gearbox and the OMANI cooling group, Auxiliary Power Unit (APU) is also fitted |
| Engine power | 1,200 bhp |
| Crew | 3 |
| Armament | Stowage for crewman-portable light anti-tank weapons, fitted with NBC protection system |

Trojan

Trojan is an armoured engineer vehicle designed to open routes through complex battlefield obstacles and clear a path through minefields.

Standard equipment includes a dozer blade, mineplough and excavator arm. Along with Titan it gives a common heavy Armoured Engineer fleet.

A Full-Width Mine Plough can be mounted at the front to clear mines and a marking system can also be fitted. It can also carry fascines to drop into ditches and tow a trailer-mounted rocket-propelled mine-clearing system.

Improved visibility is achieved by incorporating direct and indirect vision devices with low light, image intensifying and thermal imaging capabilities. The interior, and to some extent the exterior, of the vehicles have been designed around the crew station positions.

Trojan has the flexibility to support a wide range of operations, including humanitarian missions.

| Weight | 62,500 kg |
| --- | --- |
| Maximum road speed | 59 kph |
| Road range | 450 km |
| Engine | Perkins CV12 diesel engine, David Brown TN54 enhanced low-loss gearbox and the OMANI cooling group. Auxilliary Power Unit (APU) is also fitted |
| Engine power | 1,200 bhp |
| Crew | 3 |
| Armament | 1 x 7.62 mm machine gun, stowage for crewman-portable light anti-tank weapons, fitted with NBC protection system |

Challenger Armoured Repair and Recovery Vehicle (CRARRV)

The Challenger Armoured Repair and Recovery Vehicle (CRARRV) is a highly evolved armoured vehicle designed to recover and repair damaged tanks on the battlefield.

The vehicle has two winches (main and auxiliary) and an Atlas hydraulically operated crane capable of lifting a complete Challenger 2 power pack.

| Crew | 3 + 2 |
| --- | --- |
| Dimensions | 9.61 m (L) x 3.13 m (H) x 3.62 m (W) |
| Ground clearance | 0.5 m |
| Combat weight | 61,200 kg |
| Armament | 1 x 7.62 mm GPMG, smoke dischargers |
| Maximum crane lift | 6,500 kg at 4.9 m reach |
| Engine | 1,200 bhp Perkins-Condor CV12 |
| Maximum speed | 59 kph |
| Cross-country speed | 40 kph |

Samson

Spartan is a very small Armoured Personnel Carrier, it can carry four men in addition to the crew of three. It is used to carry small specialised groups such as reconnaissance teams, air defence sections and mortar fire controllers.

Samaritan, Sultan and Samson are also CVR(T) vehicles: Samaritan is an ambulance vehicle, Sultan an armoured command vehicle and Sampson is an armoured recovery vehicle.

| Crew | 2 + 10 troops |
| --- | --- |
| Dimensions | 5.16 m (L) x 2.63 m (H) x 2.48 m (W) |
| Ground clearance | 0.33 m (axles) |
| Combat weight | 10,670 kg |
| Main armament | 1 x 7.62 mm GPMG |
| Engine | 164 bhp Bedford 600 6-cylinder diesel (Cummins BT 5.1 fitted to IS variant) |
| Maximum speed | 96 kph |
| Maximum range | 510 km |

FV 434 Armoured Recovery Vehicle (ARV)

The FV 430 family of armoured vehicles entered service with the British Army in the 1960s, but regular maintenance and improvements including a new power train have enabled this old workhorse to remain in service into the 21st Century.

The FV432 can be converted for swimming, when it has a water speed of 6km/h. Properly maintained, it is a rugged and reliable vehicle with a good cross country performance.

FV 430 variants remain in service with the Infantry as command vehicles, 81mm mortar carriers, ambulances and recovery vehicles.

A recent upgrade programme has seen the delivery of over 100 uparmoured and upgraded FV430 troop carriers (Bulldog). Mechanised Infantry use the Bulldog APC as a form of protected mobility to move around the battlefield. Bulldog offers protection against small arms and artillery fire and provides good strategic and cross-country mobility.

For counter-insurgency operations the up-armoured FV430 provides a similar level of protection to Warrior and the vehicle is able to carry out many of the same tasks as Warrior, thereby relieving the pressure on heavily committed Warrior vehicles in armoured infantry battlegroups.

| Crew | 2 (commander and driver) |
| --- | --- |
| Troops | 10 |
| Dimensions | 5.25 m (L) x 2.28 m (H) x 2.8 m (W) |
| Maximum road speed | 52 kph |
| Maximum road range | 580 km |
| Fuel capacity | 454 litres |
| Engine | Rolls-Royce K60 No. 4 Mark 1-4 |
| Engine Power | 240 bhp |
| Armament | 1 x 7.62 machine gun, 2 x 3-barrel smoke dischargers |

Spartan

Same as Samson

Samaritan

Same as Samson

Sultan

Same as Samson

FV 432 Signals

Same as FV 434 CRV

FV 432 Ambulance

Same as FV 434 CRV